## Slide 1: Medium Access Control
Group 3 Naman Bhatt, Jayson Cleary, Christopher Sanders, Kushal Tiwari, Joshua Whitney

## Slide 2: The Channel Allocation Problem
How to allocate single broadcast channel among competing users?
      Static Channel Allocation
            For N users, the bandwidth is divided into N equal-sized portions.
            Works well with small, constant number of users with steady or heavy traffic.
            Doesn't work well with large and varied number of users with bursty traffic.
      Dynamic Channel Allocation
            Assumptions for Dynamic Channel Allocation: Independent Traffic, Single Channel, Observable Collisions, Continuous or Slotted Time, and Carrier Sense or No Carrier Sense.

## Slide 3: ALOHA
Pure ALOHA
  Broadcast as needed
  Listen for repeated message
  Try again if not heard back
  Any ideas on how to improve upon this?
Slotted ALOHA
  Broadcasts happen in discrete slots
  The vulnerability period is halved
  Used in cable, satellite communication and RFID

## Slide 4: CSMA Protocols
What is CSMA (Carrier Sense Multiple Access)?
  Protocols in which stations listen for the carrier and act accordingly.
  Protocols:
  1-Persistent - Station listens to channel activity, if channel is idle the station transmits, and if a collision is detected the station waits a random time before retransmitting.
  Non-Persistent - Station senses for channel activity, if channel is free station sends a frame. If the known channel is in use the station stops sensing and waits a random time before re-sensing.
  P-Persistent (Slotted channels) - Station senses if channel is free, if channel is idle the station transmits with a probablity of q = 1 - p.

## Slide 5: CSMA Protocols Cont.
  CSMA/CD
    Is the basis of Ethernet LAN.
    Similar to other protocols but with built in CD (Collision Detection).
    A collisions occurs when a device or node tries to send data at the same time another device does.
    Consists of 3 States: transmission, contention, or idle state.
    Functionality:
    Any device or node can try to send data to the channel at any time.
    If a collision is detected the frame is discarded and the device then waits a random amount of time then resends the data.

## Slide 6: Collision-free Protocol
These are protocols that are able to resolve the contention for the channel with out any collisions.
Protocols:
Bit-Map Protocol:
  Each contention period consists of N slots.
  If a station has to send a frame, a 1 is transmitted during the slot 0.
  No other station is allowed to transmit during slot 0.
  Is also known as a reservation protocol.
  Token Ring Protocol:
  Topology of the network is used to define the order in which stations send data.

## Slide 7: Collision-free Protocol
  Binary Countdown:
    More sufficient collision free protocol to handle larger networks that the previous protocols can handle due to larger overhead.
    The station broadcasts its address as a binary bit string.
    All addresses are assumed to be the same length.

## Slide 8: Limited Contention Protocols
Two way to handle this
  First is to divide stations into X groups add members to each group.
  Members in one group can only access that group slot.
  More members in a group higher chance of collision
Adaptive Tree Walk protocol
  Arranges the stations in a tree graph

## Slide 9: Wireless LAN Protocols
MACA (Multiple Access with Collision Avoidance)
  Protocol used to reduce the number of collisions by having transmitters first send a short frame to the reviver called RTS ( Request To Send)
  The receiver then sends a CTS (Clear To Send) which clears the station to transmit.
https://www.youtube.com/watch?v=t9TY0tyYGHQ