## Slide 1: Bluetooth Background
1998- Ericsson, IBM, Intel, Nokia, and Toshiba
Goal: develop a wireless standard for connecting mobile phones to other devices using short range, low-power, inexpensive wireless radios.
1999- Bluetooth 1.0 released
Allows devices to securely transfer data through pairing
Bluetooth 2.0, 3.0, and 4.0

## Slide 2
Bluetooth Architecture
Basic unit of a Bluetooth system is a piconet
1 master node- controls the clock and determines which device gets to communicate during which time slot
Up to 7 active slave nodes
Up to 255 parked nodes
Multiple piconets connected via bridge node- scatternet

## Slide 3: Bluetooth Architecture (cont.)
The master/slave design was chosen because the designers intended to design the Bluetooth chips for under $5.
The slave nodes are dumb; they do whatever the master node tells them to do

## Slide 4: Scatternet Example

## Slide 5: Bluetooth Applications
Most network protocols are generic
Bluetooth differs. It specifies particular profiles to handle different things.
  25 different applications/profiles (6 for audio and video, connecting keyboard to computer, sending images from camera to printer, mobile phone used as a remote, etc.)

## Slide 6: Bluetooth Applications (cont.)
It would have been possible to get away with 2 applications/profiles
  One for file transfer and the one for streaming real-time communication
Different working groups- each had their own applications/profiles

## Slide 7
Figure 4-35. The Bluetooth protocol architecture
The Bluetooth Protocol Stack

## Slide 8
The radio layer is the lowest defined layer of the Bluetooth specification
Moves bits from master to slave, or vice versa
Low power system
The Bluetooth Radio Layer

## Slide 9
Earlier versions of Bluetooth interfered and ruined each other’s transmissions. Solution was adaptive frequency hopping
Three forms of modulation are used to send bits on a channel
The Bluetooth Radio Layer

## Slide 10
Turns the bit stream into frames and defines some key formats
The link manager protocol sets up logical channels to carry frames between master and slave
The Bluetooth Link Layer

## Slide 11
Secure simple pairing
Synchronous Connection Oriented (SCO) link
Asynchronous ConnectionLess (ACL) link
The Bluetooth Link Layer

## Slide 12
4.6.6 The Bluetooth Frame Structure
Figure 4-36. Typical Bluetooth data frame

## Slide 13: RFID
Radio Frequency Identification

## Slide 14: EPC--What it is
A type of RFID
Short-range (10m) network
“Electronic Product Code” (High-tech barcode)

## Slide 15: How it works
Two components: “readers” and “tags”
Commands given through reader; tags obey the reader
Readers “power” the tags wirelessly
Tags either absorb signals or bounce them back to the reader

## Slide 16: Establishing a connection
Reader first broadcasts a request for tag IDs within range
Responses slotted like ALOHA
Tags respond at a random slot
    Check connection first before transmitting ID
    If reader sends the OK, respond with ID
  Slot number can be changed dynamically

## Slide 17: Operating on Tags
Once IDs are known, the reader can act on them
IDs can read and write to tags
Tags respond only with data—no headers

## Slide 18: Message Formats
Physical layers: set properties such as transfer rate
Tag Selection layers: chooses which tags to connect and allows multiple connections.
Q: Defines how many slots the tag will respond in.
CRC: Error detection

## Slide 19: Data Link Layer Switching, What it Does
Data Link Layer: Transforms raw transmission facilities into lines that appear to be free of undetected transmission errors.
  Masks the real errors so that the network does not see them
  Use of data and acknowledgement frames

## Slide 20: Learning Bridge
Learning Bridge - Bridges “Learn as they go”
  Backward Learning
Routing Procedure
  If destination port == Source port, discard frame.
  If destination port != Source port, send frame to destination port.
  If destination port not known, use flooding to send frame to all except source.
Notes: Operate in the Data link Layer

## Slide 21: Learning Bridge Diagram
Learning Bridge Connecting multiple LANs : Fig 4-41 (a)
Learning Bridge Connecting 7 Point-to-Point Stations : Fig 4-41 (b)

## Slide 22: Spanning Tree Bridge
Spanning Tree Bridge - Spanning Trees laid over topology.
“Loops in the Topology”
  overcome by ignoring some potential connections
  valid connections for a Spanning tree.
  Spanning Tree built using a distributed algo

## Slide 23: Spanning Tree Bridge Diagram
Spanning Tree Bridge with parallel Links : Fig 4-43
Spanning Tree Bridge connecting 5 bridges: Fig 4-44

## Slide 24: Repeaters, Hubs, Bridges, Switches, Routers, and Gateways
Switches - Modern bridges by another name
Bridges connect a few LANs
Modern installations tend to have point-to-point links meaning switched tend to have many ports
Which devices go in which layer : Figure 4-45 (a)

## Slide 25: VLANs
Super dry stuff

## Slide 26: Typical LANs
LANs are broken up departmental lines
All computers in a LAN connect to the same switches
Cannot easily span across long distances (buildings, cities, planets, etc.)
Physical labor overhead
Not very hip

## Slide 27: Solution: make LANs logical
  LANs no longer based on direct connection
  Any computer can be connected to any LAN on the network
  Smoother transitions for employees
  Much easier to expand/modify LANs

## Slide 28: How it works
All VLANs have a “color”
Bridge/Switch ports know which colors are on the other end

## Slide 29: IEEE’s brilliance
Backwards compatibility
Frame headers needed to include VLAN information
Only bridges and switches need use VLAN headers
Switches assign VLAN colors to each of their ports

## Slide 30: Modified headers
Slight addition to Ethernet headers